MPP 1000C Modem/850 Emulator  Page -1-     -Intro- MPP 1000C modem      capable of autodial and autoanswer.  This manual is meant to      describe the installation, use, and technical aspects of the      driver.   Major things, such as error trapping and full 850      compatibility in the -normal- everyday use that many Amodem users      and BBS Sysops would use it, as well as HomePak buyers who own      MPP modems, played a major part in the development of this      driver.  Thorough testing of this driver with Amodem 5.1,      unmodified Amis and Forem, and most important of all, HomePak,      by Russ Wetmore, to ensure full 850 compatibility has been      taking place within the past 9 months.  This driver was      constructed by the MAC/65 cartridge for the Main and Smartmodem      Source, and Basic XL for the Relocation Generator, to generate      MAC/65 source code, thus taking up a maximum of 2.5K of code      inside the machine, with the Smartmodem commands.          This introduction would not be complete without the      mentioning of the support and beta-testing help of my very good      friends.  First of all, Dave Lowry, Sysop of OTB BBS in      Oakville, Ontario, (416) 844-2483, made sure that all of the      functions of the driver worked, especially the custom XIO      commands that were built into the driver.  If it weren't for      him, this driver wouldn't have gotten the testing it has already      received.  To this day, OTB BBS is still running with this      version of the MPP driver (Without the Smartmodem commands).       Secondly, and equally important, Peter Marshall, of The Martech      Group, made sure that the Hayes SmartModem(tm) commands and XIO      commands pertaining to the 850 all worked properly.  He also      ensured that the HomePak worked properly with the driver, which      was our main goal.               -Booting up the Driver-elocatable, the booting stage of the      driver is quite simple.  All that must be done is to rename one      of the modem drivers to AUTORUN.SYS and then boot up a DOS      diskette with your new AUTORUN.SYS, that you renamed from the      driver, and when the disk driver finishes whirring, your driver      should be installed.  As the driver is relocatable, it will      place itself in the lowest area of memory without interfering      with any terminal program.  Those with the OSS Supercartridges      will have an added advantage if they are using the part of DOS      XL that puts itself into the Supercartridge, as they will save      approximately 5K, thus enabling the driver to be in a lower part      of the computer's memory.          If there is no sign of the Driver, ie. You didn't hear a      beep and see the Version number on the screen, then the driver      wasn't renamed properly.  After the driver is booted, you are      then ready to use any Terminal or Bulletin Board System (BBS)      program of your choice.                            MPP 1000C Modem/850 Emulator  Page -2-     -General CIO Calls to the Driver-ral Calls, ie. OPEN, CLOSE, PRINT,      INPUT, etc., without worrying too much about how the driver      works on the inside.  There are also specialized commands,      called XIO Commands, that will be discussed in the next section,      which communicate with the driver to get certain tasks done that      the CIO is not truly capable of handling by itself, such as      altering the Baud Rate.          The OPEN command is very simple.  All that need be done, is      to remember the Basics of the OPEN Statment.  In the OPEN      command, you need remember, that for the mode of communication,      ie. Input, OUtput or Both, a 5, 9, or 13 must be placed in the      Aux1 byte for Input, OUtput, or Both, respectively.  For true      850 compatibility, the Aux2 byte should be a zero.  A value      other than zero will give it characteristics, unique to the      driver and, thus render it incompatible with the 850 interface.       This is not a drawback, but an intention to make custom and      compact terminal and BBS programs for the MPP modem.  For the      Aux2 byte, the following corresponds to the actions taken by the      driver and the corresponding XIO statemants for you to look up      for the meanings:               +128 -- Hang up upon the CLOSE Statement (XIO      34,#chan,128,0,"R:")          +64  -- Enter Autoanswer state (XIO 35,#chan,0,0,"R:")          +32  -- No Translation (ATASCII) (XIO 38,#chan,32,0,"R:")          +16  -- Dial Number Supplied (XIO      37,#chan,0,0,"R:555-1212")          +8   -- Odd Parity (XIO 38,#chan,8,0,"R:")          +4   -- Even Parity (XIO 38,#chan,4,0,"R:")          +2   -- Echo Byte back to modem (XIO 38,#chan,2,0,"R:")          +1   -- Half Duplex (XIO 38,#chan,1,0,"R:")         desired functions in your application program, simply add up      the corresponding bytes and the modem handler will take care of      the rest.  As an example, let's say that we want to dial a      number in ATASCII and work in half-duplex:  then we add 32      (ATASCII or NO translation)+16 (Dial)+1 (Half duplex) which      comes to 49.  Thus the statement would be OPEN      #chan,13,49,"R:phonenumber" and that is all there is to it.  Due      to all of this flexibility, there are also limitations, such as      setting the Dial and Answer bits simultaneously will report back      with an error, as you can't dial and answer the phone at the      same time.  The other limitation is setting the echo & half      duplex bits simultaneously.  It won't report back with an error,      but it will constantly juggle the same bytes from both buffers.          The Get or Input statements function the same as if doing      Gets or Inputs from any other channel.  The are only two      requirements.  The first requirement is that the modem must be      plugged in.  The second one is that an XIO 40 must have been      executed for its own internal reasons, not to mention that it is      an Atari 850 standard.  For more on this, see next section.  The                   MPP 1000C Modem/850 Emulator  Page -3-     third requirement is that there must be a byte in the buffer      within a given, user presettable time period.  If any of these      three requirements are not met, then an error results, depending      on the requirement not met.  The driver doesn't lock up and wait      for you to plug in the modem.  The only condition of a lockup is      in the terminal program used, but -not in the driver-so the same as any other      Put or Print statements to the other channels.  As with the      Get/Input Statements, there are requirements to be met; however,      only the first two requirements that were listed in the      Get/Input commands are needed.  The third requirement is not      even seen by the Put/Print statments.          The CLOSE command is also the same as Closing another      device.  The only twist here is that if you had specified the      hang-up bit upon opening modem, then, when the channel is      closed, the modem will hang up and empty all of the buffers.       Otherwise, the close command will have no effect on the modem,      but will disable the XIO 40, Dial, Answer, Half Duplex,      Linefeeds and a few other things internal to the driver.                      -Special Commands (XIO) to the CIO & Modem-sed to enable a certain      characteristic, or execute a certain command in the driver.       They are XIO commands because they have nothing to do with      opening, closing, getting a status, or general I/O.  To further      explain the meaning of these Commands, we shall present them in      order and explain what the commands do.     -XIO 34 -- Switch hook toggle:-         Usage: XIO 34,#chan,aux1,aux2,"R:"          Where chan is the IOCB that you are using with the modem.     aux1 is one of the following numbers in order to have an effect      on the driver.          128 - Hangs up the modem and clears the buffer off all data in      the buffers at the time of hang-up.  The interrupt for the modem      is also disabled as it is not needed in the 'hung up' state.          192 - 'Picks up' the modem and enables the interrupt at the baud      chosen either by default or by the user (See XIO 36).          Aux2 is ignored by the driver so it may be any value.          -XIO 35 - AutoAnswer with Carrier Checking-o they may be any value.     Although no real restriction is imposed on this command and can      be used even when the modem is online, one must remember that      with all of this freedom comes a little responsibility.  What                   MPP 1000C Modem/850 Emulator  Page -4-     must be remembered is that the ring detect line is constantly      monitored until a ring pulse comes in.  What this may mean is      that you will probably think that the computer has locked up,      when it is, in fact, waiting for the ring pulse and won't      proceed without it.  -The recommended usage-is      to wait until a ring pulse is detected, by using the PEEK      function on Trig1 (DON'T use Strig(1)) located at 53265 ($D011      Hex).  This is one of the commands not found in the 850, so if      you're using an unmodified version of Amodem, etc, you won't      find any autoanswer, and certain BBS programs would need to      modified slightly, if the Smartmodem commands are not used.       However, if the smartmodem commands are used, then you wouldn't      need worry much about modification of the programs.               -XIO 36 - Changing the Baud Rate-      Where chan is, again, the IOCB used to communicate with the      modem.     Aux1 is the desired baud rate that you set using the formula of      aux1=21307/desired_baud-1.     Aux2 is ignored, thus may be any value.     As this is an XIO command used by the 850, the way in which it      is used is incompatible with the 850 itself.  However, the many      terminal programs used with the 850 have the Aux1 value below 16      and in this case, any value less than 16 will result in a      default of 300 baud, to maintain compatibility.  Conversely, any      program used with this driver setting the baud will not affect      the 850 because once XIO 40 has been executed, the 850 will      ignore the given XIO 36 command as it will tell the 850 to set      7,6, or 5 bit chars and in concurrent I/O, a full 8 bit char is      sent always.  Besides, who here speaks Baudot (raise your hand)?          -XIO 37 - Autodial-chan is the IOCB number.     Aux1 and aux2 are ignored.          The real beauty of this command is that there is really no      guesswork on how to operate this command.  All that need be      known is the phone number and that it is placed in the      quotations after the R: and the driver does the rest.  There is      no restriction as to what kind of characters may be put inside      the quotations, but you must remember that if it is in Normal      Video and is a number, the driver will use it to dial.  If you      don't want a specific number dialed, then put it in Inverse      Video.  The driver will thn ignore it.  Remember that this      command is also not found in the 850 driver.  Also, there is no                   MPP 1000C Modem/850 Emulator  Page -5-     restriction as to when this command may be used so take      precautions as to ensure that the modem is Hung up (SEE XIO 34).       The reason for this is because that there are also parts of the      driver made for the Hayes SmartModem(tm) and the Hayes does not      hang up the phone itself, and also one can, on the Hayes (As      well as this driver), use the Dial command for the Answer      command.  The only difference is that the Hayes would answer in      Originate mode only.  This doesn't really matter to the MPP      modem as it toggles Originate and Answer until it receives a      carrier.               -XIO 38 Communication Handling-Chan is the IOCB that is being used for communication with the      modem.  Aux1 is the important parameter in that it will direct      the driver as to how to communicate with the other modems.  To      explain, here is a table of what to add to aux1 in order to      achieve the desired mode of communication:          +128 -> Hangs up modem upon closing the IOCB (Not an 850      standard).     +64  -> Appends line feeds to ASCII Carriage Returns (ASCII      only).     +32  -> No Translation or Atascii mode of communication.     +8   -> Odd output parity (Not 850 Standard format)     +4   -> Even Parity in output     +2   -> Echo received bytes back to the modem (Not 850 standard)     +1   -> Half duplex (Not 850 standard)          As you may very well notice, a few of the parameters are      850 standard as they are the 99.9% of the parameters used in      most of the Terminal Programs, including HomePak.  The others      are there to perform specific task, like answering and dialing.       Chances are that you will need features not found here but are      in the 850, eg. Parity, Word Size, are slim so they were      excluded from the driver (However, one can modify the source      code provided to give you what you need).          Another thing to notice is that the ASCII mode of the      driver performs the most common ASCII to ATASCII, and vice      versa, translations:  Carriage Returns, Clear Screen, Buzzer and      Backspace.  This way, you don't have to write an ASCII      translator.         Other noticeable thing is that some of these things can be      set up upon the execution of an Open Statement.  Although this      is not 850 standard, you can save a lot of code when writing      terminal programs for the 850.  The only difference here is that      you cannot set up for line feeds in the OPen aux bytes.  This      byte is reserved for answering with Carrier Detect.                            MPP 1000C Modem/850 Emulator  Page -6-     -XIO 39 - User Timeout Setting-h the modem.       Aux1 is not used but should be a non-zero value in order to      activiate the new timeout.  Aux2 is the new timeout value in      seconds.  A zero in Aux2 will result in a 3 jiffy timeout value.       This XIO commands is useful so that the you can tell the driver      when to send you an error status.  An example for this could be      used in detecting a carrier from the XIO 35 command.  After the      preset time has expired and no carrier is present, an error is      sent back to the calling program (OTB BBS uses this method to      answer the line, if you have noticed that it may have hung up on      you before you have switched your modem to data.).               -XIO 40 - Setting up Concurrent I/O-:  XIO 40,#chan,aux1,aux2,"R:"          Where chan is the channel being used to communicate with the      modem.  Aux1 and aux2 are not needed and may thus contain any      value.  XIO 40 is needed in order to input data from the modem      as the driver uses location 747 for both buffer checks and Modem      Status.  If this command is not executed first, then an error      will result.  XIO 40 is not needed, however, for output to the      modem.  After XIO 40 is executed, the driver then performs a      check to see how many, if any, bytes are in the input buffer.       After closing the channel, XIO 40 must be executed again after      opening the channel.  XIO 40 is the only command that must be      executed after opening the modem.  However, it may be executed      before other XIO statements, unlike the 850 interface.  Also,      user supplied buffers are not supported and the buffer size is      256 bytes for both input and output, although 128 bytes for      Version 1.0H output buffer, as it is easy to keep track of them      with a one byte pointer.  When an IOCB to the modem is opened,      before XIO 40, one is able to check the status of the modem by      looking at location 747.  The following table will give the bit      positions and their purpose:          6 & 7 --> DSR (Off only when modem is unplugged)     4 & 5 --> CTS (same as above)     2 & 3 --> CRX (bit 2 is off when no carrier; otherwise, same as      above)          After XIO 40 is executed, location 747 is then used to indicate      how many bytes are in the input buffer, and location 748 is used      for indicating the number of bytes in the output buffer.          -XIO 41 - Echoing Characters to the Screen-1000C Modem/850 Emulator  Page -7-     Usage:  XIO 41,#chan,aux1,aux2,"R:"          Where chan is the IOCB used in communication with the modem.      Aux1 is a non-zero value used in order to declare the command      valid.  Aux2 is the 'decision' byte.  If it's a non-zero value,      then all characters are echoed to IOCB 0 as well as the modem.       IOCB 0 is assumed to be open and the modem will ignore any      errors and keep going if there is something wrong with IOCB 0.       This command may be executed at anytime mainly because it      doesn't deal with communication to the modem but to the default      IOCB instead.                                -Hayes SmartModem (tm) Commands- it's a smart      modem.  What it does is takes user input commands and executes      them.  These commands can be found in the drivers flagged with      an 'S' after the version number.  Although all commands are      supported, only four of them are executed:  dial, answer, repeat      last command, wait for phone to ring before answering.  All      commands are to be prefixed with the letters 'AT' and then the      command to be executed and must be less than 40 characters as      the command buffer only accepts the first forty characters.          The dial command is very simple.  All that need be done is      to enter 'ATD###', eg. ATD844-2483, and the driver will do the      rest.  For rules as to how to dial, look at XIO 37 because the      number format is the same.  The result of the command is either      'Connect' or 'No Carrier' with no error returned.          The answer command is even simpler than the dial command as      all that need be entered is 'ATA'.  The results yielded from the      command are the same as the dial command above.          The wait for ring command/answer is accomplished by typing      'ATO'.  This command puts the driver in a wait mode and will      just stay there until a ring pulse is detected.  When a ring      pulse is detected, the driver then lifts the hook as if 'ATA'      were typed in.  After that, the same results are yeilded.          All other commands will result in an 'Ok' message sent      back.  The only other time a 'No Carrier' is sent is when I/O      commands are issued and the carrier is lost.  An error 139 is      also issued once when the carrier is first lost.  When using any      SmartModem version of the driver, the XIO 39 command is disabled      as the SmartModem takes care of the timeouts.                             -Error Codes Involved with the Driver-ut (You Haven't got the modem plugged in...      All I/O involving the modem's IOCB needs the modem plugged in as      this is what the driver is designed for.)     139 -->NAK (The modem is off hook and a carrier isn't present.)     148 -->Input Buffer Empty (You tried to get bytes from the modem      and the driver waited until a specified time.  After this time,                   MPP 1000C Modem/850 Emulator  Page -8-     if no data is found in the buffer, this error will be returned      back.)     149 -->Driver Confused (You set the Dial/Answer bits in the Open      statement in the Aux2 parameters.)     150 -->Modem already Open (You tried to open two IOCB'S to the      modem simultaneously.)     151 -->Concurrent I/O error (XIO 40 was executed while the IOCB      to the modem was closed... IOCB must be opened first)     154 -->Concurrent I/O not enabled (A form of Input commands was      issued without an XIO 40 being executed previously)