One thing that drives me CRAZY aboutAtari Basic is the fact that you canonly type code in UPPER CASE. Doesthis sound familiar? You're typingalong and run across something like: 70 ?"Press any key" So you shift to lower case to typethe string. But if you're as lazy asI am, chances are that when you getto the next line, you type somethinglike: 80 get #1,a WHOOPS -ERROR!! GO BACK AND RETYPETHE LINE... Now MAC/65 doesn't mind, right? Whynot see if we can get Atari Basic tobe as forgiving?          GETTING STARTED To install NoCaps, run the Basicprogram. The machine language will beinstalled on *groan* Page Six. Beforeyou panic totally, I've posted theSource Code in this DL (NOCAPS.M65),so MAC/65 users can at leastre-assemble it to another location ifdesired. Meanwhile...            WHAT IT DOES NoCaps is activated by a USR(1536)NOCAPS.BAS does this automatically.It also POKES the memory locationthat puts the keyboard into lowercase. When you've RUN the program,issue a list command. Look at that!Basic accepts it with no problem. Hityour 'inverse' key. Type list again.Hmm...it's in lower case AND inverse,but it STILL works! What's going onhere???            HOW IT WORKS To find out, type a new line ofBasic with a line number in lowercase: 1000 dim a$(1) Now list 1000. Ah hah. Thoselowercase letters you typed have beenmysteriously transformed into UPPERCASE. THAT'S what NoCaps does. Itintercepts the INPUT, and beforeBasic gets a chance to see it, tidiesthings up so everything is 'normal'.Technical notes at the end of thisfile...            LIMITATIONS NoCaps treats just about everythingyou type the same way. It convertslower case to UPPER CASE, and stripsinverse. There's just one exception:it leaves ANYTHING CONTAINED WITHINQUOTES ALONE. That's good for typing PRINTcommands. Not so good if you type somethinglike save"d:program". In that case,DOS will try to do just that, andquickly return an error, since itdoesn't know what a "d:" (as opposedto a "D:") IS. (Actually, there's away around that, too. But that'sanother program...) Note: this ALSO means that REMstatements are converted. Well,nobody's perfect...**** NoCaps works <ONLY> in'Immediate Mode'. It's a'convenience' utility for typing inprograms. If a program is RUNning, itleaves INPUT alone.           SAFETY FIRST! Anytime you use a program like this,there's a chance for disaster. If youhave NoCaps active, and put somethingELSE on Page Six, your computer willimmediately Freeze Up the first timeyou try to type anything. (XE ownerscan usually recover from that with aRESET.) It will ALSO freeze if you try toexecute the USR command while it'salready activated. (careful with thatone.) The simplest way to disable NoCapsis just RESET. Or, you can type theBREAK key. Press it, and yourcomputer reverts to it's normal mode,and you're safe. This isn't quite perfect. MOST ofthe time, if you hit BREAK to stop aprogram scroll, it'll have no effect.(FYI, The 'disable' routine sets thekeyboard back to All Caps.) If youtype BREAK to end a program, NoCapsWILL be disabled.  To make absolutely sure you've gotNoCaps disabled, YOU SHOULD PRESS THEBREAK KEY AT A 'READY' PROMPT. OrRESET. Assuming you've left Page Six alone,you can turn NoCaps back on bycalling the USR command again: ?USR(1536) That's it. Chances are, it's notsomething you can't live without, butwhen you need it...          TECHNICAL NOTES To start, you need to know how theAtari handles it's I/O devices, whichis beyond my scope here. See MAPPINGTHE ATARI pp. 81-82 (and 221-222 inthe Revised version for XL/XEmodifications) for info on that.Please note that by using the vectortables, it's relatively easy to writea program like this that works onboth an 800 and an XE (there's alesson there!) When you call the USR routine, acouple of things happen. The addressof the E: handler table is changedfrom it's normal location in ROM, toPage Six. (The disable function worksin reverse. The address of the E:handler is changed back to it'soriginal value.) The ROM table ismoved into the NEW table, then wemake a change. Bytes 4 and 5 of anyI/O table point to the GET BYTEroutine. These are changed to pointto the NoCaps code. Anytime you're typing on your Atari,each character is saved in the systembuffer at LBUFF ($580). In the normalcourse of events, when you hitRETURN, Basic immediately takes over,and examines the contents of LBUFF,checking it for proper syntax. Butwe've put in a detour. Our NEWroutine waits for a RETURN. When itgets one, it checks LBUFF first,doing the conversions noted above.Only after it's done, does Basic getto see the line. And by then, it'sacceptable. Short and sweet. The only 'trick', is making NoCapswork in immediate mode, but notduring a RUN. Fortunately, what withall the JSR's and stuff going on atany given moment in the OS, the valueof the stack pointer is DIFFERENT inthose two cases. NoCaps knows whatthe 'immediate mode' value is. So aCMP tells it which mode Basic is in. As noted, the source code (crude asit is) can be found in NOCAPS.M65  Asalways, I hope you can improve it!Questions? Ask!!>>don                                     DDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDDD