## Slide 1: Review: Pressure Drop in PBRs
A → B -rA = kCA
dXA/dW for an isothermal ideal gas phase reaction with DP
1st order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Pressure drop (put P/P0 in terms of X)
Only for e=0
& Isothermal
0
Process is like an onion → layer built upon layer
& sometimes it makes you cry

## Slide 2: Review: Pressure Drop in PBRs
A → B -rA = kCA
dXA/dW for an isothermal ideal gas phase reaction with DP
1st order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Pressure drop (put P/P0 in terms of X)
Only for e=0
& Isothermal
0
How do we determine the reaction order?

## Slide 3: L8: Analysis of Rate Data
Goal: how to determine rate laws
In practice, collection and analysis of rate data is the most time consuming task in reactor design
BMB
Kinetics
Stoichiometry
Fluid dynamics
Reactor volume
Reactor design problem
BMB
Reactor Volume
Stoichiometry
Fluid dynamics
Kinetics
BEFORE
Reactor design problem

## Slide 4: Review of Rate Laws
The reaction:
is elementary and irreversible. Which of the following is true?
The rate cannot be determined from this information
None of the above
Ethanol and acetic acid react to form ethyl acetate and water. The rate of ethyl acetate formation is 1st order in ethanol conc and
0th order in acetic acid conc. Which of the following is true?
rethyl acetate = kCethyl acetateCwater
rethyl acetate = kCethanolCacetic acid
rethyl acetate = kCethanol
rethyl acetate = kCacetic acid
rethyl acetate = kCethanol2Cacetic acid-1
Cacetic acid0 (zero power) = 1

## Slide 5: Collection & Analysis of Rate Data
Constant-volume batch reactor
  For homogenous reactions
  Concentration vs. time measurements
  Measurement during the unsteady-state operation
Differential reactor
  For solid-fluid reactions
  Measurement during steady state operation
  Product concentration is usually monitored for different feed conditions
Data collection is done in the lab, where we can simplify BMB, stoichiometry, and fluid dynamic considerations
  Goal: determine reaction order, a, and specific reaction rate constant, k, in the rate law
Want ideal conditions → well-mixed (data is easiest to interpret)
Select a simple reactor

## Slide 6: Method of Excess
A + B → products Suspect rate eq. -rA = kCAaCBb
Run reaction with an excess of B so CB ≈ CB0
Rate equation simplifies to –rA = k’CAa where k’=kACBb ≈ k’=kACB0b and a can be determined
Repeat, but with an excess of A so that CA ≈ CA0
With excess A, rate simplifies to –rA = k’’CBb where k’’=kACAa ≈ k’’=kACA0a
Determine kA by measuring –rA at known concentrations of A and B, where

## Slide 7: Analysis Methods
Differential method
Integral method
Half-lives method
Initial rate method
Differential reactor
More complex kinetics

## Slide 8: Differential Method
0
0
Where –rA = kCAa
alpha power
Determine dCA/dt from plot by graphical or numerical methods
Plot ln(-dCA/dt) vs ln CA
Average slope
Slope = a
To find k, find the value of –dCA,p/dt that corresponds to a specific concentration CA,p. Raise CA,p to the a power and divide into –dCA/dt)p
Hey, we just jumped from step a to step c. How do we get dCA/dt?
Plot DCA/Dt as a function of t

## Slide 9: Graphical Method
dCA/dt is read using the value where the curve crosses a specified time
Plot DCA/Dt vs t
Draw rectangles on the graph. Then draw a curve so that the area above the curve that is cut off of each rectangle approximately fills the unfilled area under the curve
0
t1
t2
(-DCA/Dt)t=0
(-DCA/Dt)t=1
(-DCA/Dt)t=2

## Slide 10: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt
8 | 0 |  |  |  | 
4 | 1 |  |  |  | 
2 | 2 |  |  |  | 
1 | 3 |  |  |  | 

## Slide 11: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt
8 | 0 | 1-0=1 |  |  | 
4 | 1 | 2-1=1 |  |  | 
2 | 2 | 1 |  |  | 
1 | 3 |  |  |  | 

## Slide 12: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt
8 | 0 | 1 | 4-8= -4 |  | 
4 | 1 | 1 | 2-4= -2 |  | 
2 | 2 | 1 | 1-2= -1 |  | 
1 | 3 |  |  |  | 

## Slide 13: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt
8 | 0 | 1 | -4 | 4
4 | 1 | 1 | -2 | 2
2 | 2 | 1 | -1 | 1
1 | 3 |  |  | 
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt
8 | 0 | 1 | -4 | 4 | 
4 | 1 | 1 | -2 | 2 | 
2 | 2 | 1 | -1 | 1 | 
1 | 3 |  |  |  | 
-

## Slide 14: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt
8 | 0 | 1 | -4 | 4
4 | 1 | 1 | -2 | 2
2 | 2 | 1 | -1 | 1
1 | 3 |  |  | 
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt
8 | 0 | 1 | -4 | 4 | 4.5
4 | 1 | 1 | -2 | 2 | 2.55
2 | 2 | 1 | -1 | 1 | 1.35
1 | 3 |  |  |  | 0.5
-

## Slide 15: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt
8 | 0 | 1 | -4 | 4 | 4.5
4 | 1 | 1 | -2 | 2 | 2.55
2 | 2 | 1 | -1 | 1 | 1.35
1 | 3 |  |  |  | 0.5
Slope = a
-
Plot ln(-dCA/dt) vs ln CA

## Slide 16: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt | ln(-dCA/dt) | ln(CA)
8 | 0 | 1 | -4 | 4 | 4.5 | 1.5 | 2.1
4 | 1 | 1 | -2 | 2 | 2.55 | 0.9 | 1.4
2 | 2 | 1 | -1 | 1 | 1.35 | 0.3 | 0.7
1 | 3 |  |  |  | 0.5 | -0.7 | 0
Slope = a
= 1.0
Plot ln(-dCA/dt) vs ln CA
-rA= (0.6/time)CA

## Slide 17: Graphical Method Example
CA | t | Dt | DCA | -DCA/Dt | -dCA/dt
8 | 0 | 1 | -4 | 4 | 4.5
4 | 1 | 1 | -2 | 2 | 2.55
2 | 2 | 1 | -1 | 1 | 1.35
1 | 3 |  |  |  | 0.5
Slope = a
Differential Method
Only for irreversible reactions
Advantages: 1 experiment
Disadvantages: can only handle simple kinetics
-
-

## Slide 18: Analysing methods
Differential method
Integral method
Half-lives method
Initial rate method
Differential reactor
More complex kinetics

## Slide 19: Integral Method
A trial-and-error procedure to find reaction order
Guess the reaction order → integrate the differential equation
Method is used most often when reaction order is known and it is desired to evaluate the specific reaction rate constants (k) at different temps to determine the activation energy
Looking for the appropriate function of concentration corresponding to a particular rate law that is linear with time

## Slide 20
For the reaction A  products
For a first-order reaction - rA = k CA
ln (CA0/CA)
t
For a second-order reaction - rA = k CA2
1/CA
t
For a zero-order reaction -rA = k
CA
t
Plot of CA vs t is a straight line
Plot of ln(CA0/CA) vs t is a straight line
Plot of 1/CA vs t is a straight line

## Slide 21: Analysis Methods
Differential method
Integral method
Half-lives method
Initial rate method
Differential reactor
More complex kinetics

## Slide 22: Method of Half-lives
The half-life of a reaction, t1/2, is defined as the time it takes for the concentration of the reactant to fall to half of its initial value
By determining the half-life of a reaction as a function of the initial concentration, the reaction order and specific reaction rate can be determined

## Slide 23: Method of Half-lives
The half-life of a reaction, t1/2, is defined as the time it takes for the concentration of the reactant to fall to half of its initial value
By determining the half-life of a reaction as a function of the initial concentration, the reaction order and specific reaction rate can be determined

## Slide 24
A  products
ln (t1/2)
ln CA0
Slope = 1- 
Plot ln(t1/2) vs ln CA0. Get a straight line with a slope of 1-α

## Slide 25: Analysis Methods
Differential method
Integral method
Half-lives method
Initial rate method
Differential reactor
More complex kinetics

## Slide 26: Method of Initial Rates
When the reaction is reversible, the method of initial rates can be used to determine the reaction order and the specific rate constant
Very little product is initially present, so rate of reverse reaction is negligible
  A series of experiments is carried out at different initial concentrations
  Initial rate of reaction is determined for each run
  Initial rate can be found by differentiating the data and extrapolating to zero time
  By various plotting or numerical analysis techniques relating -rA0 to CA0, we can obtain the appropriate rate law:

## Slide 27: Example: Initial Rate Method
4HCl + CaMg(CO3)2  Mg2+ + Ca2+ + 4Cl-+2CO3 + 2H2O
The dissolution of dolomite using hydrochloric acid:
Concentration of HCl at various times was determined from atomic
absorption spectrophotometer measurements of the Ca2+ and Mg2+ ions
CHCl
t
4 N HCl
1 N HCl
Make a plot of ln (-rA0) vs ln CA0
The slope = a

## Slide 28
Evaluating the mole balance on a constant V batch reactor at t = 0:
ln (CHCl)
ln (-rHCl,0)
Slope = 
Plot of ln (-rHCl,0) vs ln CHCl,0 will give reaction order a & k

## Slide 29: Analysis Methods
Differential method
Integral method
Half-lives method
Initial rate method
Differential reactor
More Complex Kinetics

## Slide 30: Differential Reactors
The criterion for a reactor being differential is that the conversion of the reactants in the bed is extremely small, as is the change in reactant concentration through the bed
Reactant concentration through the reactor is essentially constant (i.e. the reactor is considered to be gradient-less)
Can treat the mole balance like a CSTR
Rate of reaction determined for a specified number of pre-determined initial or entering reactant concentrations
Determine rate of reaction as a function concentration or partial pressure
Operate isothermally
CA0
CAe
CA
CA0 ~ CA~ CAe

## Slide 31: Differential Catalyst Bed
The rate of reaction per unit mass of catalyst, r’A
flow rate in - flow rate out + rate of generation = rate of accumulation
When constant flow rate, u0 = u:
Product concentration
The reaction rate is determined by measuring product concentration, Cp

## Slide 32: More Complex Kinetics
Carry out batch experiments
Use optimization software to compute kinetic parameters by least squares (covered in process control)
Investigate errors by calculating standard deviations of parameters and looking at magnitudes of ra,meas,i –rA, calc,i to look for outliers (will learn in process design, this is FYI for this class
If parameters are sufficiently accurate, then stop. If not, keep repeating the procedure
Sum of squares difference between the measured values and calculated values