## Slide 1: Review: Growth of Silicon Film by CVD
Write out elementary reactions and assume a rate-limiting step
1. Adsorption
Rate of adsorption = rate of attachment – rate of detachment
2. Surface reaction:
Si
Si
Si
Si
Si
H
H
Si
Si
Si
Si
Si
H
H
Si
Si
Si
Si
Si
adsorption
Surface
reaction
fv & fSiH2: fraction of the surface covered by vacant sites or SiH2, respectively
Surface coverage is in terms of fraction of surface, not conc of active sites

## Slide 2: Review: Growth of Germanium Films by CVD
Gas-phase dissociation
Adsorption (1)
Adsorption (2)
Surface reaction
Surface reaction is believed to be the rate-limiting step:
ks: surface specific reaction rate (nm/s)
fH2: Fraction on the surface occupied by H2
fGeCl2: fraction of the surface covered by GeCl2
Germanium films have applications in microelectronics & solar cell fabrication
Rate of Ge deposition (nm/s):
*Surface coverage is in terms of fraction of surface, not conc of active sites

## Slide 3: Review: Catalyst Deactivation Kinetics
Adjustments for catalyst decay need to be made in the design of reactors
Catalyst activity a(t) is used as a quantitative specification
Catalyst activity at time t:
Reaction rate for catalyst used for time t
Reaction rate for fresh, unused catalyst
For fresh, unused catalyst,
Rate of consumption of reactant A on catalyst used for time t is:
a(t): time-dependent catalyst activity k(T): T-dependent specific rate constant
fn(CA, CB…etc): function of gas-phase conc. of reactants, products & contaminants
Rate of catalyst decay:
Function of activity
Temperature-dependent specific decay constant
Functionality of rd on reacting species conc. h=1: no conc dependence; h=Cj: linearly dependent on concentration

## Slide 4: Review: Types of Catalyst Deactivation
    3. Poisoning: molecules (product, reactant or impurity) irreversibly bind to the active site
  1. Sintering (aging): loss of active surface due to high temperature
Second-order decay of reaction rate with respect to present activity:
Catalyst activity at time t:
Sintering decay constant:
    2. Coking or fouling: carbonaceous material (coke) deposits on surface
Concentration of carbon on surface (g/m2):
Catalyst activity at time t:
A, n & m: fouling parameters
a(t): time-dependent catalyst activity
kd: specific decay constant
CP: concentration of the poison

## Slide 5: Review: Moving-Bed Reactor
Reactant & catalyst enter at top of reactor
Reactant & catalyst flow down the length of the reactor together as a plug
Product and spent catalyst (black) flow out of reactor outlet
Spent catalyst is regenerated by passing it through a separate regeneration unit, and newly regenerated catalyst is fed back into the top of the reactor
When catalyst decay occurs at a significant rate, they require frequent regeneration or replacement of the catalyst
Moving-bed reactor enables continuous regeneration of spent catalyst
Operates in the steady state, like a PBR

## Slide 6: Review: Moving-Bed Reactor Design
Reactants
u0 (dm3/s)
fresh catalyst US (g/s)
Z
Z + DZ
W
W + DW
Products & coked catalyst
Catalyst flow US << reactant flow u0
As far as the reactants are concerned, the reactor acts like a PBR:
Find -da/dW and dXA/dW. Will need dt/dW.
Relate t to US:
Multiply dt/dW by -da/dt to get –da/dW:
If the rate of consumption of A for catalyst used for time t:

## Slide 7: Guidelines for Deducing Mechanisms
More than 70% of heterogeneous reaction mechanisms are surface reaction limited
If a species appears in the numerator of the rate law, it is probably a reactant
If a species appears in the denominator of the rate law, it is probably adsorbed in the surface

## Slide 8
Suggest a mechanism and rate-limiting step that is consistent with the rate law
The overall reaction for the hydrogenation (H) of ethylene (E) over a cobalt-molybdenum catalyst to form ethane (A) is H2(g) + C2H4(g) → C2H6 (g) and the observed rate law is:
PE appears in the denominator of the observed rate eq, so PE is adsorbed on the surface. Neither PH or PA are in the denominator, so neither H or A are adsorbed on the surface.
We’ll assume that the surface reaction is rate limiting
No desorption step - PA isn’t in the denominator. Eliminate conc of occupied & vacant sites on surface:

## Slide 9
The experimental data for the gas-phase, catalytic, irreversible reaction A + B→C is given in the table. Suggest a rate law & mechanism consistent with the data.
Run | PA (atm) | PB (atm) | PC (atm) | -r’A(mol/g∙s)
1 | 0.1 | 1 | 2 | 0.073
2 | 1 | 10 | 2 | 3.42
3 | 10 | 1 | 2 | 0.54
4 | 1 | 20 | 2 | 6.80
5 | 1 | 20 | 10 | 2.88
6 | 20 | 1 | 2 | 0.56
7 | 1 | 1 | 2 | 0.34
8 | 1 | 20 | 5 | 4.5
Approach: Use graphs to show how -r’A varies with Pi when Pj and Pk are held constant
Chart: PA (atm)
| 0.1 | 1 | 10 | 20
PA vs rate | 0.073 | 0.34 | 0.54 | 0.56
Chart: PB (atm)
| 1 | 10 | 20
PB vs rate | 0.34 | 3.42 | 6.8
Chart: PC (atm)
| 2 | 5 | 10
PC vs rate | 6.8 | 4.5 | 2.88
We need to use these graphs to determine whether A, B, & C are in the numerator, denominator, or both.

## Slide 10
The experimental data for the gas-phase, catalytic, irreversible reaction A + B→C is given in the table. Suggest a rate law & mechanism consistent with the data.
Run | PA (atm) | PB (atm) | PC (atm) | -r’A(mol/g∙s)
1 | 0.1 | 1 | 2 | 0.073
2 | 1 | 10 | 2 | 3.42
3 | 10 | 1 | 2 | 0.54
4 | 1 | 20 | 2 | 6.80
5 | 1 | 20 | 10 | 2.88
6 | 20 | 1 | 2 | 0.56
7 | 1 | 1 | 2 | 0.34
8 | 1 | 20 | 5 | 4.5
Approach: Use graphs to show how -r’A varies with Pi when Pj and Pk are held constant
Chart: PA (atm)
| 0.1 | 1 | 10 | 20
PA vs rate | 0.073 | 0.34 | 0.54 | 0.56
-r’A increases rapidly at low PA (means its in the numerator), but it levels off at high PA (means its in the denominator)→ PA in numerator & denominator of -r’A

## Slide 11
The experimental data for the gas-phase, catalytic, irreversible reaction A + B→C is given in the table. Suggest a rate law & mechanism consistent with the data.
Run | PA (atm) | PB (atm) | PC (atm) | -r’A(mol/g∙s)
1 | 0.1 | 1 | 2 | 0.073
2 | 1 | 10 | 2 | 3.42
3 | 10 | 1 | 2 | 0.54
4 | 1 | 20 | 2 | 6.80
5 | 1 | 20 | 10 | 2.88
6 | 20 | 1 | 2 | 0.56
7 | 1 | 1 | 2 | 0.34
8 | 1 | 20 | 5 | 4.5
Approach: Use graphs to show how -r’A varies with Pi when Pj and Pk are held constant
Chart: PA (atm)
| 0.1 | 1 | 10 | 20
PA vs rate | 0.073 | 0.34 | 0.54 | 0.56
Chart: PB (atm)
| 1 | 10 | 20
PB vs rate | 0.34 | 3.42 | 6.8
-r’A increases linearly as PB increases → PB is only in the numerator

## Slide 12
The experimental data for the gas-phase, catalytic, irreversible reaction A + B→C is given in the table. Suggest a rate law & mechanism consistent with the data.
Run | PA (atm) | PB (atm) | PC (atm) | -r’A(mol/g∙s)
1 | 0.1 | 1 | 2 | 0.073
2 | 1 | 10 | 2 | 3.42
3 | 10 | 1 | 2 | 0.54
4 | 1 | 20 | 2 | 6.80
5 | 1 | 20 | 10 | 2.88
6 | 20 | 1 | 2 | 0.56
7 | 1 | 1 | 2 | 0.34
8 | 1 | 20 | 5 | 4.5
Approach: Use graphs to show how -r’A varies with Pi when Pj and Pk are held constant
Chart: PB (atm)
| 1 | 10 | 20
PB vs rate | 0.34 | 3.42 | 6.8
Chart: PC (atm)
| 2 | 5 | 10
PC vs rate | 6.8 | 4.5 | 2.88
-r’A ↓ with ↑PC→ rnx is irreversible so PC must be in the denominator of -r’A. Therefore, C is adsorbed on surface

## Slide 13
The rate law suggested for the experimental data given for the gas-phase, catalytic, irreversible reaction A + B→C is:
Suggest a mechanism for this rate law.
PA and PC are in the denominator. A (reactant) and C (product) must be adsorbed on the surface, but B is not adsorbed on the surface:
Adsorption of reactant A:
Desorption of product C:

## Slide 14
The rate law suggested for the experimental data given for the gas-phase, catalytic, irreversible reaction A + B→C is:
Suggest a mechanism for this rate law.
PA and PC are in the denominator. A (reactant) and C (product) must be adsorbed on the surface, but B is not:
Adsorption of reactant A:
Desorption of product C:
Surface reaction step: B is not adsorbed on the surface, so B must be in the gas phase when it reacts with A adsorbed on the surface.
The overall reaction is irreversible, so this step is likely irreversible.

## Slide 15
The rate law suggested for the experimental data given on slide 14 for the
gas-phase, catalytic, irreversible reaction A + B→C is:
Suggest a mechanism for this rate law.
Adsorption of reactant A:
Desorption of product C:
Surface reaction:
Postulate that the surface reaction is the rate limiting step since that is true the majority of the time. Check if that is consistent with the observed kinetics
Eliminate CA∙S & Cv
from rate eq
Insert into site balance and solve for Cv

## Slide 16
The rate law suggested for the experimental data given on slide 13 for the gas-phase, catalytic, irreversible reaction A + B→C is:
Suggest a mechanism for this rate law.
Adsorption of reactant A:
Desorption of product C:
Surface reaction:
Postulated surface reaction is rate limiting